## Slide 1: Camera Alert System

## Slide 2
Alert
System
Cameras
MQTT
Messages
every 10 mins
Mailjet
Operator
MQTT
Broker
Cloudflare
Mailjet API
Email
Unsubscribe link in email
Secure Channel
Mark MacIntyre’s
rms_mqtt system
Alert System
Database

## Slide 3
ALERT SCENARIOS Three independent alert scenarios are implemented. 1 Camera Status Down Triggered when camerastatus=0 for longer than timeout_minutes. 2 Pi and Camera Silent Triggered when no MQTT messages are received for silence_timeout_minutes. 3 Has Not Rebooted Triggered when lastboot timestamp exceeds reboot_threshold_hours. Each scenario: • Sends an initial email • Sends reminders every 24 hours (configurable) • Auto-unsubscribes after a configurable number of repeats

## Slide 4: Examples of emails sent out

## Slide 5
Station NZ0014 has not rebooted recently.
Don't reply to this email
Your station last booted at (UTC): 2025-12-29 08:10:11 UTC
Hours since boot: 78.02
There may not be anything wrong. It may only be confused.
1) Log into your pi/computer. Look in the RMS_Data folder. Look for a file called ".reboot_lock". You may need
to go to View/Show Hidden in the menu to see this file. Files that begin with a dot are hidden files.
If you are using the command line, use "ls -la to see hidden files. If you see this file delete it.
2) Reboot the pi/computer. Try to do this gracefully at the command line (sudo reboot) but power cycle it if
you must. Everything will probably be OK after a reboot but if this error reoccurs, ask us for help.
If you are unsure, please reach out to
gmn@mckellar.net.nz (gmn@mckellar.net.nz)
steve@matheson.net.nz (steve@matheson.net.nz)
Unsubscribe from these alerts:
https://alerts.mckellar.nz/unsubscribe?station=NZ0014&email=gmn%40mckellar.net.nz&sig=59f62add8b8ccec4e6e7bbc6b691ae1739e152dd95b80b09e8b9d2402e28bf3a
Note: the link will open a confirmation page before you are unsubscribed.
​

## Slide 6
Camera alert for station NZ0014
Don't reply to this email
No messages have been received since:
2025-12-31 03:14:24 UTC
This indicates that your whole system is offline.
Things to check:
1/ Is the power on to the devices?
2/ Is the internet on? Are you having trouble with other devices on the network?
3/ Is the wifi connection still good? You may need to put a keyboard, mouse and
keyboard onto the pi/computer to check this.
If you are unsure, please reach out to
gmn@mckellar.net.nz (gmn@mckellar.net.nz)
steve@matheson.net.nz (steve@matheson.net.nz)
Unsubscribe from these alerts:
https://alerts.mckellar.nz/unsubscribe?station=NZ0014&email=gmn%40mckellar.net.nz&sig=59f62add8b8ccec4e6e7bbc6b691ae1739e152dd95b80b09e8b9d2402e28bf3a
Note: the link will open a confirmation page before you are unsubscribed.
​

## Slide 7
Camera alert for station NZ001P
Don't reply to this email
No messages have been received since: 2025-12-31 03:14:20 UTC
This indicates the camera is not connected to the pi/computer.
Things to check
1/ Is the power switched on to the POE injector, which powers the camera.
2/ Are all the connections intact. Detach and replug all the ethernet connectors.
3/ Check the ethernet cables are plugged in the right places. On the POE injector
the two ports are labelled POE & LAN. The cable to the camera goes into POE and
the cable to the raspberry pi goes into LAN.
4/ Check the lights. There should be one light on the POE injector. It should be solid on.
If it is flashing then the POE injector is in an error state.
5/ Check the lights on the POE splitter. One blue light indicates power is on. A green
light occasionally blinking indicates network traffic.
6/ Is the POE splitter warm to the touch. This may indicate a failed POE splitter.
These don't fare well when exposed to the weather. Ask for a replacement if it appears
to have failed.
7/ Inside the camera housing, check that all the plugs are well seated on the camera board.
There is one small plug for power, one larger one for data. A third plug that is loose is OK.
If you are unsure, please reach out to
gmn@mckellar.net.nz (gmn@mckellar.net.nz)
steve@matheson.net.nz (steve@matheson.net.nz)
Unsubscribe from these alerts:
https://alerts.mckellar.nz/unsubscribe?station=NZ001P&email=gmn%40mckellar.net.nz&sig=f3133d58d87d01f052d48e6c4c25f08f80278394a9e6513610535444b17c8a1c
Note: the link will open a confirmation page before you are unsubscribed.
​

## Slide 8: Important URLs
https://github.com/pmcke/Alerts
https://github.com/markmac99/rms_mqt